# Guide for assembly of paper model Volkswagen Golf R32

We begin with preparation Works. I recommend to print model on paper 160g. We make axles A of lenght 54 mm from skewer or from 2 mm thick hard steel wire. I fastened with glue parts 24 and 25 one time. After some experience I discovered, that it is good to fasten with glue also ribs 20 and 21 and part 26. We lay line A-A and B-B on back side of parts 1 and 2. When we are bonding bumpers, we are guided by central lines on separate parts which help their symetricity towards longitudal axis of model.

We bond together parts 1, 2 and 3. We are bonding roof to shrouds of model from rear to front. We bond part 4 to part 3. We bond hood 5 from front to rear. Part 4 is bonded only with part 3 and hood 5 is only covering it, so do not bond it with part 4. We bond face 6 from center to sides. Window 7 is bonded first to roof, then to shrouds 1 and 2. We bond parts 8 and 9 from center to sides. Part 10 must be placed downward with printed (black) side and narrow curving element is curved softly up. We are keeping this angle and controlling it according to lower edge of part 9. Part 11 is bonded to part 10 (from center) and its triangular corners of part 11 are curved up according to lower edge of trunk doors. Part 12 is bonded from center to sides. We bond part 13L (left) and 13P (right) to part 12. We bond lower element of part 14 to part 12 first, and then step by step towards edges of part 13L and 13P. When glue is dry we form edges and lower element of whole piece to final appearance like bow. Parts 15L and 15P are bonded to parts 12, 13L and 13P step by step from mudguard to center of bumper. After perfect drying we bond this piece to part 9, to lower edge of taillights. Then we start with front bumper. We bond together parts 16 and 17 from center to sides. After drying we can bond these to face 6. When group of parts 18 and 19 completely dry we bond it with part 17, also first center then sides. Finally we bond sides of front bumper to mudguards in the parts 1 and 2. We bond part 42 into rear bumper.

Now the raw part of body is complete and we continue with chassis. We bond parts 20 (rear) and 21 (front) to lines on inside sides of parts 1 and 2. We bond axle holders and after drying we bond them into body according to picture guide to parts 20 and 21. We bond parts 24 and 25 to parts 22 and 23. Part 24 is also bonded by sides to front bumper 17. We must bond part 26 carefully, because we can fix any faults in symmetry, but we can also make it worse.

We control any possible screw of body from front and rear view.

We bond door-frame sills 27 and bars 28, both are divided to P (right) and L (left), on the sides of body. We bond wiper 29 to rear window, and wipers 30L and 30P on front windshield. On sides 1 and 2 are bonded sign-posts 31. We bond carefully edges of mudguards 32L (left) and 32P (right) from front to rear. We bond spoiler 33 to edge of rear window and roof, so spoiler is bonded with glue mainly to rear roof and partially by sides to parts 1 and 2.

We make exhaust tips and we bond it to holes in parts 14 and also to part 25. We bond handles 37 on doors and emblem 38 on trunk doors. Next step is to make and bond edges of rear mudguards 39, same method as with front.

We finish body with bonding of outer rearview mirrors 34 and 35.

We bond 4 wheels from parts 40, 41 and 43. We bond these on two axles A (54mm), painted black.

In order to not moving wheels from side to side we coil narrow stripes of paper on axles, so papers works like distance  rolls which are making pressure on axle so wheels can not move from side to side, but they can be rotated freely.

I would like to thank Marek Lalík and Monika Kamenicka for this guide and supporting advices.

Author of the model: Ľ. Papánek

Translated by Dušan Gaži.